## Slide 1: High-precision measurement of the neutron EDM
Construction and characterization of the main B0 magnet for the nEDM@SNS experiment
Alexandra Klipfel
Faculty advisor: Brad Filippone

## Slide 2: Overview of nEDM@SNS
Goal: measure neutron electric dipole moment () to an uncertainty of cm
Will be operated at the Spallation Neutron Source (SNS) at Oakridge National Laboratory
  Should come fully online in 2028 or 2029
Current accepted value:
  nEDM@SNS represents a significant improvement in sensitivity by ~2 orders of magnitude
(Pendlebury et al. 2015, Phys. Rev. D)
Notes: And a little later on I will address why this is the case and how we expect to increase the precision so dramatically

## Slide 3: Motivation
Long history of searches for EDMs of various particles, nuclei, and molecules
  ~60 years of history for nEDM measurements
Goal: explore and test Beyond Standard Model (BSM) theories
  Proposed BSM scenarios address issues like dark matter and the baryonic asymmetry of the universe
  These theories provide new, unobserved mechanisms of CP violation which generate EDMs
Thus, the observation of EDMs would indicate the existence of these CP violating mechanisms and lend support to BSM theories
Notes: So, therefore if we want to probe beyond the standard model and search for evidence of these theories, this is a very important realm of experimentation.

## Slide 4: nEDM@SNS Methods
Interaction Hamiltonian for spin ½ particle with electric dipole moment () and magnetic dipole moment ():
Spin precession with angular Larmor frequency:
Relate to change in Larmor frequency if field is reversed relative to field:
Expected statistical uncertainty:
Takeaway—we want to maximize: , observation time (), and number of observations ()
Notes: in this case "parallel" indicates that the electric field is parallel to the magnetic field.
I am going to explain how the nEDM@SNS experiment prpposes to maximize these three quantities.

## Slide 5: nEDM@SNS Methods
We use Ultra-Cold Neutrons (UCN)
  Energies neV total reflection from certain solid materials
  Produced by exposing liquid 4He to a beam of cold neutrons
    Long storage time: allows maximization of and
    4He is a great electrical insulator: allows maximization of
“Co-magnetometer”: polarized 3He
  In solution in the superfluid 4He at low concentrations
  3He precession frequency has no E-dependence
    Thus, it acts as a reference to measure magnetic field in the same volume inhabited by the UCN
    Key idea: compare 3He precession frequency with UCN frequency as E field is changed
big improvement in the uncertainty compared to past experiments
Notes: Acts as a co-magnetometer because it allows us to measure the magnetic field in the volume occupied by the neutrons.
3He has negligible E dependence—EDM is screened by atomic electrons

## Slide 6: nEDM@SNS Methods
3He absorbs UCN, causes 4He to produce measurable UV scintillation light
Absorption cross-section (and therefore scintillation rate) is highly spin-dependent
  Maximized when the spins are antiparallel
  Thus, scintillation rate depends on Larmor frequencies of 3He and UCN
  Changing the E field should result in a change to the UCN frequency, and therefore a change in the scintillation rate that is directly related to the neutron’s EDM value
Key takeaway: We measure the UV scintillation intensity for different applied electric fields and from this, we can extract the value of the nEDM
Notes: Measure the scintillation light with a wavelength-shifting dye that coats the neutron-impermeable walls of the UCN storage chambers

## Slide 7: Breakdown of Experiment
CRYO-VESSEL
Ahmed et al. 2019, JINST
Notes: Components are being built at several universities
Experiment will be assembled and run at Oakridge National Labs

## Slide 8: Caltech’s Role
Prof. Filippone’s group is constructing and testing the cryogenic vessel and B0 magnet system
Cryo-vessel: will house the two measurement cells, detectors, magnet systems, shielding…
  Cools everything < 7 K
Ahmed et al. 2019, JINST
Notes: Lead goes superconducting at ~7.2K
The vessel is ~15-20 feet high

## Slide 9: My specific project: B0 magnet
Magnet’s Purpose: generate a uniform T DC holding field inside the vessel for spin precession
  Aligned horizontally in x direction
Goal: uniform field gradients
  < ~5ppm/cm
How do we achieve this?
  Electromagnetic shielding layers
  Mechanically impose desirable boundary conditions
  External Helmholtz coils to cancel geomagnetic field (on the order of T)
Cross-cut of cryo-vessel
B0 magnet coil schematic
B0 MAGNET AND SHIELDING LAYERS
Ahmed et al. 2019, JINST
Notes: So the B0 magnet is one of the magnet coils that sits inside the cryo-vessel
other coils are AC for field
manipulation
All the shielding and coils are nestled in the cryo-vessel like layers of an onion

## Slide 10: Timeline
Construction
  Assemble G10 frame
  Wind copper wire coil
  Lead shielding panels
  Copper-coated G10 panel
  Metglas shield
  Superconducting lead endcaps
  Insert into cryovessel
  Test vacuum and cooling systems
Characterization
  Measurement campaign #1
  Remove magnet and make any required fixes
  Measurement campaign #2
Pack and Ship to Oakridge
B0 magnet frame and coil
Dimensions: cylinder 8 ft high, 6.5 ft in diameter
Modified saddle-shaped coil
  Currently wound with copper wire
  Will be wound with superconducting wire (NbTi) on site at Oakridge
This assembly was finished before I joined the group
Highly uniform T field Larmor frequencies near 100 Hz
Ahmed et al. 2019, JINST
Notes: We want uniformity for two reasons:
1. to maintain the polarization of the neutrons and 3He atoms
2. to minimize a systematic false EDM signal that’s induced by motional magnetic field effects
What is G10—a fiberglass material
-can control which directions thermal contraction occurs therefore when this gets cooled the components shrink in a uniform way we understand

## Slide 11: Timeline
Construction
  Assemble G10 frame
  Wind copper wire coil
  Lead shielding panels
  Copper-coated G10 panel
  Metglas shield
  Superconducting lead endcaps
  Insert into cryovessel
  Test vacuum and cooling systems
Characterization
  Measurement campaign #1
  Remove magnet and make any required fixes
  Measurement campaign #2
Pack and Ship to Oakridge
Superconducting Lead Panels
DONE
DONE
Cylindrical shield of 0.8mm thick high-purity lead
  Constructed in 6 separate panels
Wrapped around the outside of the magnet coil
Purpose: shield from external time-varying fields
  Shielding is due to the Meissner Effect when the lead goes superconducting
  External flux is expelled from the interior of the superconductor
Notes: We constructed the six panels in September

## Slide 12: Timeline
Construction
  Assemble G10 frame
  Wind copper wire coil
  Lead shielding panels
  Copper-coated G10 panel
  Metglas shield
  Superconducting lead endcaps
  Insert into cryovessel
  Test vacuum and cooling systems
Characterization
  Measurement campaign #1
  Remove magnet and make any required fixes
  Measurement campaign #2
Pack and Ship to Oakridge
Copper Shield
DONE
DONE
DONE
The spin-dressing coil generates an AMF which would induce eddy currents and unacceptable heating in the Metglas shield
  Thus, copper shield goes between B0 & Metglas and spin-dressing coil
Shield geometry: cylindrical G10 panel with m Cu coating
Shielding is due to eddy currents in Cu sheet
  Because thickness << skin depth (~7 cm /)
In progress: measuring the Cu shielding factor and the effect of soldering separate panels together to make the big panel
Notes: Gap because commercial copper-clad G10 sheets don’t come in the size we need
We soldered copper foil to connect the gap
Previous models and simulations reveal that the majority of the shielding comes from the eddy currents with the greatest diameter and therefore the greatest flux.
Thus, just the top and bottom 10 inches is suffiecint for 95-99% of shielding

## Slide 13: Timeline
Construction
  Assemble G10 frame
  Wind copper wire coil
  Lead shielding panels
  Copper-coated G10 panel
  Metglas shield
  Superconducting lead endcaps
  Insert into cryovessel
  Test vacuum and cooling systems
Characterization
  Measurement campaign #1
  Remove magnet and make any required fixes
  Measurement campaign #2
Pack and Ship to Oakridge
Metglas Shield
DONE
DONE
DONE
IN PROGRESS
Flux return just outside the B0 coil
  Made of Metglas 2826M, an amorphous material which retains its high permeability at low temperatures
Purpose: improve B0 field uniformity
  Mitigates errors in wire placement
  Reduces field distortions due to superconducting lead shielding layer
Notes: Imposes a boundary condition s.t. that the field lines terminate perpendicular to the shield
--helps improve uniformity
--”sucks in” the field lines

## Slide 14: Timeline
Construction
  Assemble G10 frame
  Wind copper wire coil
  Lead shielding panels
  Copper-coated G10 panel
  Metglas shield
  Superconducting lead endcaps
  Insert into cryovessel
  Test vacuum and cooling systems
Characterization
  Measurement campaign #1
  Remove magnet and make any required fixes
  Measurement campaign #2
Pack and Ship to Oakridge
Superconducting Lead Endcaps
DONE
DONE
DONE
IN PROGRESS
JANUARY
The lead shield is essentially a closed cylinder, capped on both ends
Purpose: Ensure uniformity of B0 field
  Field lines will run parallel to the superconductor
  Essentially removes fringe fields so the coil behaves as if it’s infinite
Still designing and constructing some components—installation by February
TOP ENDCAP

## Slide 15: Timeline
Construction
  Assemble G10 frame
  Wind copper wire coil
  Lead shielding panels
  Copper-coated G10 panel
  Metglas shield
  Superconducting lead endcaps
  Insert into cryo-vessel
  Test vacuum and cooling systems
Characterization
  Measurement campaign #1
  Remove magnet and make any required fixes
  Measurement campaign #2
Pack and Ship to Oakridge
Measurements
DONE
DONE
DONE
IN PROGRESS
JANUARY
FEBRUARY?
JANUARY
Measure the three field components at many points in the interior
  Then reconstruct the internal field with Maxwell-guided fits
  Use a robotic probe-arm with x,y,z direction magnetometers
    Can insert the probe into the “warm bore” which provides access from the outside
  Will have to characterize and correct for background fields
Perform 1-2 rounds of measurements with full cooldown
Goal is to ship to Oakridge in March-May 2022

## Slide 16: Timeline
Construction
  Assemble G10 frame
  Wind copper wire coil
  Lead shielding panels
  Copper-coated G10 panel
  Metglas shield
  Superconducting lead endcaps
  Insert into cryovessel
  Test vacuum and cooling systems
Characterization
  Measurement campaign #1
  Remove magnet and make any required fixes
  Measurement campaign #2
Pack and Ship to Oakridge—March - May
Summary
DONE
DONE
DONE
IN PROGRESS
JANUARY
FEBRUARY
MARCH
JANUARY
Driving goal of nEDM@SNS is to measure the neutron’s electric dipole moment with unprecedented precision
  Searching for evidence of CP violating BSM physics
Caltech is developing the cryogenic system and B0 magnet
  Uniformity of the B0 magnet is very important
    Goal: < 5 ppm/cm
    Accomplish this various layers of shielding
  I will work on constructing the magnet and shielding and characterizing its field
FEBRUARY?
JANUARY

## Slide 17
Ahmed et al. 2019, JINST

## Slide 18
Ahmed et al. 2019, JINST